# Text boxes

Where no range is stated, treat data as typical rather than absolute

Data Sheet	Drilling Starch exceeding

OCMA DFCP 5 specs and

API 13A, Section 11 (May 1,1993)

Drilling Starch / Non fermenting

Description	low viscous fluid loss reducer

Modification and base	modified potato starch

Appearance	free flowing, granular white powder

Compatibility	all drilling fluids

Solubility/Dispersibility	readily without lump forming

excellent suspensibility

Properties

Bulk density	650 - 700gr/l

Others	resistant to high concentrations of salt

(sodium, potassium) and calcium compounds.

Stability	suitably preserved with environmental

friendly biocide, stable against bacteria

Particle size	< 2000 micron

Application	Fluid Loss reducer for all types

of drilling fluids

Typical laboratory and field data are available for evaluation.

Rate of addition	10 - 30 kg/m3	(4 – 11 ppb)

Storage	store dry, 12 months

Packing	25kg or 50lbs net paper bags with PE coating.

special packing like jungle boxes; optional

Safety Precautions	None. Refer to Safety Datasheet.